OPERATION AND MAINTENANCE MANUAL FOR

B-36 AND B-42 BENDING MACHINE

BEFORE OPERATING THE MACHINE,

READ THIS MANUAL AND MAKE SURE YOU UNDERSTAND HOW THE MACHINE OPERATES

CONTENT

1.  MACHINE OPERATION						Page 3

2. SPECIFICATIONS							Page 4

3. CONTROL PANEL							Page 5

4. OPERATION METHODS						Page 7

4.1. Manuel Operation

4.2. Automatic Operation

4.3. Emergency Stop

5.  MAINTENANCE							Page 8

6. TROUBLE SHOOTING						Page 9

6.1. PLC and Troubleshooting

7. ELECTRICAL DIAGRAM						Page 11

READ THIS MANUAL AND MAKE SURE YOU UNDERSTAND HOW THE MACHINE WORKS BEFORE OPERATING THE MACHINE

CAUTIONS !

To prevent from serious injuries, the employers and owners must provide neccesary protections and equipments for installations and operations. The employers and owners must also provide thorough training courses for the operators and they must carefully supervise all operations and obey the following safety regulations:

1. DO NOT LET UNTRAINED PERSON OPERATE THE MACHINE. THIS MACHINE CAN BE OPERATED ONLY BY THOSE WHO ARE WELL-TRAINED AND FULL UNDERSTAND THE FEATURES AND SPECIFICATIONS OF THE MACHINE AS WELL AS SAFETY RULES FOR OPERATING THE MACHINE.

2. DO NOT PUT ANY PORTION OF YOUR BODY ON ANY MOVING COMPONENT OF THE MACHINE. DO NOT ENTER THE WORK SPACE OF THE MACHINE UNLESS THE POWER OF THE MACHINE IS OFF. KEEP AWAY WHILE THE MACHINE IS OPERATING.

3. DO NOT WEAR LOOSE CLOTHING OR GLOVES SINCE THEY MAY BE TANGLED IN THE MACHINE. TIGHTEN YOUR CLOTHES, ESPECIALLY THE CUFFS.

4. ALWAYS CLEAR THE TURNING TABLE AND REMOVE THE SCRAPS BEFORE START TO OPERATE

5. TO ADJUST A NEW WORK PIECE, ALWAYS OPERATE THE MACHINE IN MANUAL MODE.

6. MAKE SURE THAT THE FLOOR WHERE THE MACHINE AND THE OPERATOR STAND ARE STURDY

7 DO NOT OPERATE THE MACHINE TO BACKWARD POSITION WHILE WORK PIECE, BENDING BAR AND SUPPORT ARE ON THE TURNING TABLE. ALSO REMOVE THE BENDING TOOLS AND SUPPORT BEFORE PUSHING RESET BUTTON.

2. SPECIFICATIONS:

| Bending Capacity | 36 mm | Weigth | 380 Kg |
| --- | --- | --- | --- |
| Voltage | 380 V | Dimension L X B X H | 800 X 950 X 900 mm |
| Power | 3 KW | Output Rpm | 11 d/d |
| Rpm | 1500 rpm |  |  |

| Capacity Table |
| --- |
| Parça Sayısı | 1 | 2 | 3 | 4 | 6 |
| Çelik Kalitesi | 45 kg/mm2 | 36 | 24 | 20 | 18 | 14 |
|  | 65 kg/mm2 | 28 | 22 | 18 | 14 | 12 |
|  | 85 kg/mm2 | 26 | 20 | 16 | 12 | 10 |

| Number | Part Name |
| --- | --- |
| 1 | Turning Table |
| 2 | Support |
| 3 | Sled |
| 4 | Bending and Center Bar |
| 5 | Cover |
| 6 | Control Panel |
| 7 | Foot Pedal |

| Number | Item | Function |
| --- | --- | --- |
| 8 | Return-back Switch | Makes the turning table return back to stop switch (3) when triggered by one of the angle pins (5). |
| 9 | Stop pin | Triggers stop switch (3) |
| 10 | Stop Switch | Determines the machine reference-starting point |
| 11 | Support | - |
| 12 | Angle Pin | By changing its place, it enables different angles |
| 13 | Center Bar | - |
| 14 | Bending Bar | Bends the work piece |

3. CONTROL PANEL

|  | KONTROL ADI | AÇIKLAMA |
| --- | --- | --- |
| 15 | ON – OFF RİGHT LEFT | Turning table can work both clockwise (CW) and counter-clockwise (CCW). This button is also turns on and turns off the machine. Right or left position turns the machine. The middle position of the button turns off the machine. Within a few seconds later the button turned on, 4 leds start to blink. That means the machine is ready for new operation. The right and left positions may swap according to machines electrical connection. |
| 16 | AUTOMATIC MANUEL MODE | Enables for the user to operate manually and automatically. On manuel mode, the machine works if thee foot pedal is being pushed. When return back sqitch (8) is triggered, turning table returns back to its first position countinously. On automatic mode, machine works if the foot pedal is pushed once and returns back. When arranging the machine for a new work, always use manuel mode. |
| 17 | First Lamb (For wide angle) | When pushed, machine stops according to the third pin and returns back to first position. |
| 18 | Second Lamb (Perpendicular angle) | When pushed, machine stops according to the second pin and returns back to first position. |
| 19 | Third Lamb (For acute angle) | When pushed, machine stops according to the third pin and returns back to first position. |
| 20 | Program | When program button is selected, after the foot pedal is pushed, the machine returns to back after third pin. On second push of foot pedal, the machine returns back after second pin. The machine repeats that movement 2 times more with every foot pedal pushes. Lastly, third pin will be active when the foot pedal pushed. After that 4 movements machine repeats the same procedure countinously. Program is available on the automatic mode. In program active bending light will blink.. |
| 21 | Emergency Button | Stops the machine immediately. Check weekly whether the emergency button works without any problem. |

4. OPERATION METHODS

4.1. MANUEL MODE

Clear off the work piece (rebar which will be bended) and bending parts on the turning table (1). Remove the cover (5)

Turn manuel – automatic button (16) on to manuel mode. Choose the way (CCW or CW) with the on off button (15). Place the pins as you wish according to the angles you want. Push one of the angle buttons (17, 18 or 19). Make sure that the light is on when you push.

Keep Push foot pedal till it makes the angle you want. The machine will be return back continously to its beginnig position. If the foot pedal is pushed when the turning table returns back, the machine will stop. If the foot pedal is pushed again, the machine will continue again its operation.

4.2. AUTOMATIC OPERATION

Turn manuel – automatic button (16) on to automatic mode. Push one of the angle buttons (17, 18 or 19). After the foot pedal is pushed, the machine returns to first switch and then stop switch.

4.3. EMERGENCY STOP

Do not hesitate to push emergency stop in any emergency case. In case emergency stop is pushed, and the turning table stops between stop and return – back switches, the machine will return to the stop switch whenever the foot pedal is pushed. Therefore, remove the parts on the turning table before working again the machine.

After emergency button is pushed, please follow the following procedures:

- Remove the bended rebar. Clear off the turning table.

- If the rebar is stucked, release the slades as shown in the following picture.

- And then you may continue to usual operation after restart the machine.

5. MAINTENANCE

| Remove the rebar dust and dirt. | Daily |
| --- | --- |
| Oil the sadles | Daily |
| Remove the center pin (13) and clear its hole | Daily |
| Remove the cover and clean the switches | Daily |
| Make sure the emergency button works | Weeks |

6. TROUBLESHOOTING:

| Problem | Solition | Description |
| --- | --- | --- |
| Machine is not working | Check on off button is on | Make the on off button right or left |
|  | Check emergency button | Release the emergency button |
|  | Check the electricity connections (Main cable, foot pedal cable) | Remove all electricty connections and plug them again |
|  | Check the electricity is 380 V | Check 3 phases |
|  | Contact electricty specialist |  |
|  | Cable is too long | Do not use cable over 50 meters. |
| Machine makes noise and works hardly | Check whether there is anything blocks the turning table | Romove the cover and check the switches work fine. |
|  | Check the electricty cable. | Shorten the cable. |
|  | Check the motor | If the motor is hot, the promblem may be motor. Contact electricty specialist. Do not work the machine. The motor may burn. |
| Machine does not work sometimes | Foot pedal may not work | Open the foot pedal. Make it short circuit. Or change the foot pedal switch. |
|  | Check whether the voltage is not low | Change the electricity |

6.1. PLC (Programable Logic Control) AND TROUBLESHOOTING

Please find the following PLC diagram. Plc controls the machine and input / output commands. Some problems may be confirmed with the leds on the plc. On the following image, “I/O indicators” show the operation of some parts of the machine. These parts are as follows:

Right – Left Button (15)

Automatic Manuel Button (16)

Angle Buttons (17, 18, 19)

Program Buttons (20)

Foot Pedal (7)

Stop Switch (10)

Return Back Switch (8)

Working of these parts may be checked on the PLC leds. Trigger the part (e.g. push the foot pedal or trigger a switch). If no led is blinking, the part you are checking may be faulty.

Also make sure that  “RUN/STOP” switch is on. If no led is on, the plc may be broken or the transformer does not transmit electricity. In that case, consult an electricity specialist.

7. ELECTRICTY CONNECTIONS

# Text boxes

15

7

6

5

4

3

2

1

16

17

18

19

20

21