OPERATION AND MAINTENANCE MANUAL FOR

H-36 AND H-42 HYDRAULIC CUTTING MACHINE

READ THIS MANUAL AND MAKE SURE YOU UNDERSTAND HOW THE MACHINE WORKS BEFORE OPERATING THE MACHINE

CAUTIONS !

To prevent from serious injuries, the employers and owners must provide neccesary protections and equipments for installations and operations. The employers and owners must also provide thorough training courses for the operators and they must carefully supervise all operations and obey the following safety regulations:

1. DO NOT LET UNTRAINED PERSON OPERATE THE MACHINE. THIS MACHINE CAN BE OPERATED ONLY BY THOSE WHO ARE WELL-TRAINED AND FULL UNDERSTAND THE FEATURES AND SPECIFICATIONS OF THE MACHINE AS WELL AS SAFETY RULES FOR OPERATING THE MACHINE.

2. DO NOT PUT ANY PORTION OF YOUR BODY ON ANY MOVING COMPONENT OF THE MACHINE. DO NOT ENTER THE WORK SPACE OF THE MACHINE UNLESS THE POWER OF THE MACHINE IS OFF. KEEP AWAY WHILE THE MACHINE IS OPERATING.

3. DO NOT WEAR LOOSE CLOTHING OR GLOVES SINCE THEY MAY BE TANGLED IN THE MACHINE. TIGHTEN YOUR CLOTHES, ESPECIALLY THE CUFFS.

4. MAKE SURE THAT THE FLOOR WHERE THE MACHINE AND THE OPERATOR STAND ARE STURDY

SPECIFICATIONS:

| Cutting Capacity | 36 MM | 42 MM |
| --- | --- | --- |
| Voltage | 380 V | 380 V |
| Power | 5,5 HP | 7,5 HP |
| Weight | 350 KG | 450 KG |
| Dimension | 1500X680X880 | 1500X680X880 |
| Output Rotation | 1500 RPM | 1500 RPM |
| Rotation | 1500 RPM | 1500 RPM |
| Production Date |  |  |
| Serial No |  |  |

Always decide how many pieces to cut according to the following table and the table on the machine

| 36 HYDRAULİC CUTTİNG MACHİNE | 42 HYDRAULİC CUTTİNG MACHİNE |
| --- | --- |

: Yuvarlak Malzeme   : Kare Malzeme  : Dikdörtgen Malzeme

OVERVIEW :

| 1 | Oil-in Tap | To add up oil. The adviced oil is 68 No. hydraulic oil |
| --- | --- | --- |
| 2 | Control Lever | It works backward and forward to operate the machine |
| 3 | Base | It arranges the gap to cut different size iron bars |

| 1 | Oil-Out Tap | To pour out the oil in order to renew it. |
| --- | --- | --- |
| 2 | Main Power Switch and fuse |  |
| 3 | Power Switch | It turns on and turns off the machine |

OPERATING THE MACHINE:

- Before the operation, tighten the bolts seen in the following picture (Picture 3).

(Picture 3)

- And also arrange the base according to the iron bars to be cut. This arrangement is vitally important for blades of the machine (Picture 4).

(Picture 4)

- Be sure that the blades bolts are also tightened.

- Turn on main switch and power switch. NOTE THAT POWER SWITCH WORKS 2 DIRECTIONS, RIGHT AND LEFT. SELECT THE PROPER DIRECTION ACCORTDING TO THE ELECTRICITY CONNECTION OTHERWISE MAHCHINE MAY NOT OPERATE.

- Be sure that it is not used very long cable for the electricity. The adviced maximum cable lenght is 50 meters.

- Put the iron bar to be cut and by using control lever forward and backward, cut the iron bar. Do not force the machine after finishing the cutting backward or forward direction unnecessarily. This action will force the hydraulic system itself.

- After release the control lever, the hydraulic piston will go back spontaneously. If you want it go back fastly, you may also use the control lever backward direction to shorten the time to go backward position.

- İMPORTANT: The machine has many oil nozzles put on different places. For less maintenance, failure and breakdown, OİL THE MACHİNE DAILY.

- DO NOT PUT ANY PORTION OF YOUR BODY ON ANY MOVING COMPONENT OF THE MACHINE. DO NOT ENTER THE WORK SPACE OF THE MACHINE UNLESS THE POWER OF THE MACHINE IS OFF. KEEP AWAY WHILE THE MACHINE IS OPERATING.

MAINTENANCE:

ALWAYS KEEP THE MACHINE CLEAN

| Remove the dust and scraps on the machine | Daily |
| --- | --- |
| Oil the nozzles | Daily |
| Renew the hydraulic oil (Oil no: 68 or equivalent one.) | 6 months |
| Check the oil level | Once a week |
| Remove the dust and scraps on the machine | Daily |

TROUBLESHOOTING:

| PROBLEM | POSSIBLE SOLUTION | DESCRIPTION |
| --- | --- | --- |
| Machine is not working | Check both the main switch and power switch is on |  |
|  | Check the electrical connection, main cable. | Remove all the connections and put them again |
|  | Check the electricity 380 V | Check 3 phases |
|  | Advise an electricity specialist |  |
|  | Make sure that the oil level is fine |  |
|  | Turn the main switch to other direction. | There may be reverse electricity connection. Turn the main switch to the other direction and retry to operate the machine |
| Machine makes too much noise and works hardly | Make sure there is nothing that prevents machine’s working |  |
|  | Check the cable cord. | If it is too long, shorten the cord and try again. The adviced cord lenght is 50 meters. |
|  | Check the motor. | If it is too hot, there could be a problem with the motor and hydraulic pump |
|  | Check the oil | In time, the oil loose its specialty. It is needed to be renewed periodically. On hot wheathers, the oil becomes thin and it may affect the machine performance |
|  | Check the blades | Blades may become worn out or the blade bolts are loosed. Change with the new one or change the cutting side and tihgten the bolts, |
| Machine leaks hydraulic oil |  | Hydraulic machines leak some oil. It is natural. But if it leaks too much, maintenance is needed. Thighten the joints where the oil may leak. It may also caused by the felts of the hydraulic cylinder. If it is the case they should be renewed in time. |

MONTAJ RESMİ